BJX2 Display Overview
Overview of the display subsystem for my BJX2 core prototype.

---
Major Sub-Modes
- Color Cell
  - Various cell formats with different properties.
  - Each cell is 128 or 256 bits.
  - Can represent either a character cell or graphics.
- Bitmap
  - Each pixel is encoded directly.
  - Can give high quality, but needs a lot more memory.
- Controlled via a Screen Mode MMIO register.

---
Screen Memory
- Screen Memory starts at 0xF00A0000, up to 128K
  - Can also be configured as 32K or 64K
  - As MMIO, it is DWORD based, not byte addressable.
- Screen memory is in BRAM, not DRAM
  - The amount of BRAM available depends on the FPGA.
    - Thus, no high-resolution bitmap graphics.
  - Redrawing the screen requires low latency and high bandwidth.
    - This made the use of Block-RAM preferable.
- Typically, things are drawn off-screen, and then the resultant image is copied over.
  - This may involve the use of a color-cell encoder.

---
Screen Layout
- Screen is organized as a grid of cells, starting in the top left corner.
- Screen resolution can be effected by changing the number of rows and columns, within the limits of the existent screen memory.
  - 40x25 gives 320x200 with 8x8 cells.
  - 80x50 gives 640x400 with 8x8 cells.
  - 100x37 gives 800x296 with 8x8 cells.
    - Or, 800x592 with 8x16 cells.
- Modes exceeding available screen memory may result in the screen contents wrapping around.

---
Screen Registers (1)
- Screen registers are located at 0xF00BFF00
- Screen Mode is register 0.
  - Bit 0: 80/100 columns vs 40/50
  - Bit 1: Reduce cells to 128 bits (HalfWidth).
    - Precludes using 256-bit cell formats.
  - Bit 2: Use 50 rows vs 25.
  - Bit 3: Use 800x600 vs 640x400 as base resolution.
    - Selects 50/100 columns vs 40/80.
  - Bits (7:4): Screen Mode
    - 0, 8: Color Cell, 0=YUV, 8=RGB
    - 1, 9: Bitmap (16bpp), 1=YUV, 9=RGB
    - 2, A: Bitmap (4bpp RGBI)

---
Screen Registers (2)
- Screen registers 1..7 are reserved for now.
  - Note that VGA timings are hard-coded in the hardware.
- Screen register 8 is a frame number.
  - This is written by the program on frame advance.
- Screen registers C..F allow storing into Font SRAM.
  - The register selects which of the four WORDs to store into.
  - The high bits of the stored value give the index.
  - The low bits of the stored value give the WORD value to be stored.

---
Color-Cell Modes
- Each cell has a major mode and submode.
  - Given by the high order 2 bits of the first two DWORDs.
- 0.x: Text Cells
  - Pair of colors, attribute bits, font and character.
- 1.x: Basic Graphics (low-detail, historical)
- 2.0: 8x8x1 (128-bit)
- 2.2: 8x8x2+UV4x4x2 (256-bit, YUV 4:2:0)
  - Defines a YUV space cube for the 8x8 cell.
- 3.1: 8x16x1 (256-bit), color pair per 4x8 sub-cell
- 3.2 4x8 (256-bit), color pairs per 2x2 sub-cell
- 3.3 8x8 (256-bit), color pairs per 4x4 sub-cell

---
Text Cell Modes, 0.x and 1.x
- Laid out as a character cell.
  - (31:30)=Tag
  - (29:28)=Color Mode
  - (27:22)=Color B (6-bit, RGB222)
  - (21:16)=Color A (6-bit, RGB222)
  - (15:10)=Attribute Flags (0.x, Text Cells)
  - ( 9: 8)=Font Selector (0.x)
  - ( 7: 0)=Character Glyph (0.x)
  - (15: 0)=Pixel Bits (1.x)

---
Text Cell Modes (Cont)
- Font 0: ASCII / CP-437 (ROM Font)
- Font 1: Graphical Symbols (ROM Font)
  - 00..7F: Partition Patterns (Similar to those in BC7)
  - 80..FF: PETSCII style extended symbols
- Font 2/3: User Font SRAM (512 glyphs, 8x8)
  - Note: 1C0..1FF: Also used as a 256 color palette.
    - Each 64b glyph contains four 16-bit colors.
- Attributes:
  - (15:14): Blink (None, Fast, Slow, Blink Alternate/Reverse)
  - (12): Overline
  - (11): Underline
  - (10): Strike-through

---
Color Cell Mode 3.3
- DWords 0..3: Pairs of CLR15 endpoints.
  - CLR15: YVU654 or RGB555, depending on Screen Mode.
  - Each DWORD contains a pair of colors (A and B)
  - The high 2 bits of each DWORD are tag bits, or MBZ.
- DWords 4..7: Endpoint Selection
  - 2 bits per pixel, interpolating between associated endpoints.
  - 00=B, 01=(2/3)B+(1/3)A, 10=(1/3)B+(2/3)A, 11=A
  - Each DWORD is a 4x4 sub-block.
- Format is conceptually similar to DXTn / BCn texture compression.

---
Color Cell Mode 3.1
- Overall cell layout is basically the same as 3.3
  - Just each sub-block is 4x8 pixels rather than 4x4
- Main difference is that, in the sub-blocks, each 2-bit selector is instead a pair of 1 bit selectors.
  - High bit applies to even scanlines.
  - Low bit applies to odd scanlines.
  - 0=B, 1=A

---
Bitmap, Mode 4x4x16bpp
- Whole screen uses a bitmap mode.
- Each 256-bit cell holds a 4x4 block of pixels.
  - The pixels are in raster order starting from the LSB.
  - This allows easy copying from a linear framebuffer.
  - Each pixel is in Pixels are either YVU655 or RGB565 (depending on screen mode)
    - YVU655: (15:10)=Y, (9:5)=V / Cr, (4:0)=U / Cb
    - RGB565: (15:11)=R, (10:5)=G, (4:0)=B
- Setting Half Width cells will use 4x4x8bpp indexed color (256 color via palette)
  - Screen mode selects if palette colors are YUV or RGB.

---
Bitmap Mode, 8x8x4bpp
- Reuses the same basic layout as the 4x4 mode.
  - Each 16-bit unit is split into 4 pixels (2x2 block)
  - These sub-block pixels are similarly in raster order.
  - Each 4-bit pixel holds an RGBI value (i, r, g, b)
    - Functionally analogous to the VGA 4bpp modes.