BJX2 Core
Stuff related to the BJX2 CPU Core effort.

---
Pipeline
- IF, Instruction Fetch
  - Get instructions from I-Cache
  - Figure instruction lengths.
- ID1, Instruction Decode 1
  - Decode the instruction words.
- ID2, Instruction Decode 2 (Register Fetch)
  - Fetch registers from register file.
  - Prepare ops to be executed.
- EX1, Execute 1
  - Execute simple ops or submit values to other units.
- EX2, Execute 2
  - Gather results of executed ops from other units, block until operations complete.
- WB, Write-Back
  - Store register values back into register files.

---
IF: Instruction Fetch
- Fetches a block (say, 64 or 96 bits) from the I$.
- Logic in the I$ Fetch may infer the length of the fetched instruction.
  - PC needs to be advanced by the next clock edge.
  - Doing this in ID1 would be 1 cycle late.
    - Alternately, would need to update based on future ops.
- WEX: Length covers the whole block.
  - Decode/Execute for WEX works per block.

---
ID1: Decode 1
- Matches the bit patterns for the instructions, unpacking them into a collection of fields.
  - Major Command, Predication Mode
  - Bits for Sub-Op / Memory Access Type / …
  - Register IDs (Rs, Rt, Rn)
  - The decoded Immediate value.
- Run multiple decoders in parallel.
  - Logic selects the output from the appropriate decoders for the output lanes.
  - WEX uses multiple 32b decoders in parallel.

---
ID2: Decode 2
- Fetches the contents of the various registers from the register file.
- Things like the immediate value, etc, may be treated as registers here. The RF is supplied the values to return for these registers.
  - This allows being able to handle nearly all operations as register operations internally.
- This stage may also handle things like pipeline interlocks, etc.
  - All ops in a WEX block are handled in lockstep here. So, an interlock or stall will be applied to all of the lanes at the same time.

---
EX1: Execute 1
- Execute simple operations directly.
  - The results here are simply forwarded to EX2.
- ALU ops, Multiply, etc, are submitted to their respective units.
  - The results will be gathered back in EX2.
- This stage also computes the memory address and initiates a memory Load or Store.
  - EX1 may assert a "held" register (for an op which will complete later), which may be seen by the interlock logic. Some other outputs may also trigger an interlock.
- During interlock, ID2 → EX1 simply produces NOPs while the earlier pipeline stages are kept stalled; allowing EX2 to finish up the operation before advancing.

---
EX2: Execute 2
- Gathers up the results from the various units, outputting them to their respective destination registers.
- Triggers pipeline stalls, as needed, in the case of slower ops or memory access.

---
WB: Writeback
- Gets the results of the execute stages written back to the register file.
- For WEX, this means consolidating the results from multiple write ports.
  - This can be done, eg, via parallel register arrays (for individual write ports) with multiplex being done on fetch (selecting the value from the array holding the current register value).
  - Can also be done via discrete registers, and logic to multiplex the input values during write-back.

---
Interlocks
- An instruction in EX1 may sometimes not produce a result directly, but only after EX2 completes.
  - An operation waiting in ID2 may depend on the result produced in EX2.
  - Simply advancing the pipeline would result in an op landing in EX1 and seeing a stale value for a given register.
- We may need to insert a "bubble" into the pipeline to allow operations to see the intended values.
  - The EX and WB stages advance, whereas the IF and ID stages do not.
  - EX1 receives a NOP whenever the ID stages are held but the EX stages are not.

---
Forwarding
- Register results may be moved forwards along the EX pipeline and are stored back to registers during WB.
- Registers may be accessed from earlier in the pipeline before the values have been written back to the register file.
  - Special logic is added to deal with these registers.

---
WEX Register Ports (1)
- Each lane has 2 read ports and 1 write port.
  - If enough lanes are used, the values read from the destination registers will be implementation dependent.
  - If fewer lanes are used, each op will behave as-if it had 3 read ports available.
  - Generated code should not depend on specific register aliasing behavior.
- Note that a scalar core will have 3 read ports and one write port.

---
WEX Register Ports (1)
- Each lane has 2 read ports and 1 write port.
  - If enough lanes are used, the values read from the destination registers will be implementation dependent.
  - If fewer lanes are used, each op will behave as-if it had 3 read ports available.
  - Generated code should not depend on specific register aliasing behavior.
- Note that a scalar core will have 3 read ports and one write port.

---
WEX Register Ports (2)
- Read/Write ports
  - WEX2-2W: Rs, Rt, Ru, Rv → Rm, Rn
  - WEX2-3W: Rs, Rt, Ru, Rv, Rx, Ry → Rm, Rn, Ro
- 1-Wide Case:
  - WEX2-2W: Rs, Rt, Rv → Rm
  - WEX2-3W: Rs, Rt, Ry → Rm
- 2-Wide Case:
  - WEX2-2W: Ru, Rv, xx | Rs, Rt, xx → Rn, Rm
  - WEX2-3W: Ru, Rv, Rx | Rs, Rt, Ry → Rn, Rm
- 3-Wide Case:
  - WEX2-3W: Rx, Ry, xx | Ru, Rv, xx | Rs, Rt, xx → Ro, Rn, Rm

---
WEX Register Ports (3)
- In invalid combinations of operations, the registers may alias in an implementation defined manner.
  - An implementation is neither required to detect nor trap in these cases.
- If operations are performed which are not allowed in a given lane, or within a given combination of instructions, the resultant behavior will be undefined.
  - An implementation is neither required to detect nor trap in these cases.